## Slide 1
Sensors
Summary of data collection using remote sensors
v2
Thomas Bryden
9 April 2025

## Slide 2
Overview
Sensor
Microcontroller
Physical property to measure
Temperature
Gas concentration
Distance
etc.
1
Send data
To local storage
Via mobile network
To central location
etc.
2
3
4
Connections and communication
2 power lines (positive & negative)
1-4 communication lines
Power supply
5

## Slide 3
1. Sensor

## Slide 4
1.a Sensor
Sensor measures a physical quantity and converts it to a communication protocol (communication protocols are described in slide 2.b)
The method of converting physical property to communication protocol varies for every sensor and depends on the physical quantity being measured
Each sensor needs to be supplied with power wires (1 positive and 1 negative) and communication wires (see slide 2.a)
Small circuits may be required next to the sensor:
Sensor purchased from Bosch
Small circuit next to sensor, in this case made by the company Pimoroni but could be done yourself
Output to microcontroller

## Slide 5
Physical property to measure | Communication protocol to convert to
Ultrasonic distance | RS232
Physical property to measure | Communication protocol to convert to
Humidity, pressure, temperature | I2C
1.b Sensor examples
MaxBotix SCXL-MaxSonar-WR
Bosch BME280
Sensor measuring physical property
Communication and power from microcontroller
Sensor measuring physical property
Communication to microcontroller
Power from microcontroller
Small local circuit

## Slide 6
2. Connections and communication

## Slide 7
2.a Connections and communication
Sensor needs to be connected to the microcontroller using power and communication wires
The microcontroller may be located right next to the sensor on the same circuit board, or could be further away and a wire connects the two
Power wires:
  Two wires required, one for positive and one for negative
  If the sensor is low power, it may be powered directly from the microcontroller. If more power (or higher voltage) than the microcontroller can deliver is required, a separate power supply circuit is needed
Communication, see next slide

## Slide 8
2.b Communication
Number of communication wires depends on the sensor communication protocol used (which is determined by the sensor manufacturer, see slide 1.b)
The physical quantity measured by the sensor is converted to bits by the sensor manufacturer and then the communication protocol determines how these bits are sent to the microcontroller
Common communication protocols include:
  I2C https://circuitbasics.com/basics-of-the-i2c-communication-protocol/
  SPI https://www.circuitbasics.com/basics-of-the-spi-communication-protocol
  UART https://www.circuitbasics.com/basics-uart-communication/
Sensor
Microcontroller

## Slide 9
3. Microcontroller

## Slide 10
Contain all components on single chip
Cons: Less powerful than full computer
Pros: Smaller, cheaper, uses far less power
Well suited for remote sensing applications
3.a Microcontroller
Permanent memory
(SSD)
CPU
Temporary memory (RAM)
Full Computer
Microcontroller

## Slide 11
Microcontroller program is written on a regular computer and then uploaded to the microcontroller where it runs in a loop
Remote connections*:
  Cannot remotely connect whenever you want, as listening for remote connections uses microcontroller power
  When the microcontroller wakes up it can check if anyone wants to connect, or check for program updates
Typical microcontroller program structure
3.a Microcontroller use
1. Connect to sensor and read data, see slide 2.b
2. Connect to internet
3. Send API POST request, containing sensor measurement, to website
4. Check website to see if any updates to program are available, if yes, download updates
5. Go to sleep for a set amount of time
*This is my experience, not sure on how this works in industry

## Slide 12
3.b Microcontroller examples
ESP32
Arduino
STMicroelectronics
Whereas a Raspberry Pi is a full computer, not a microcontroller, requires more power
Texas Instruments

## Slide 13
4. Send data

## Slide 14
1. Store locally on memory card | Need to physically collect data
2. Transmit via Wi-Fi | May not be a Wi-Fi connection available
3. Transmit via mobile network | Requires signal and mobile network usage costs
4. Transmit via radio frequency | Requires computer in another location to receive data
4.a Send data
Depends on location and available connections
4G

## Slide 15
4.b Send data POST request
How I send data from the sensor to the database, may be different in industry
Microcontroller
Standard POST request:
bespokesensors.com/databases/post-sensor.php?api_key=XXX&temperature=21.26&humidity=85
Hosted webpage
bespokesensors.com/databases/post-sensor.php
Extract api_key and sensor data from POST
Use api_key to work out which table to insert sensor data into
Generate SQL query to insert data into table
Execute SQL query, data stored in database
String httpRequestData = "api_key=" + apiKeyValue + "&temperature=" + String(temperat) + "&humidity=" + String(humidity) + "";
if ($_SERVER["REQUEST_METHOD"] == "POST") {
…
$sensor_sql_init = "INSERT INTO " . $table . " (";
…
…
if ($sensor_conn->query($sensor_sql) === TRUE) {

## Slide 16
4.c Send data via radio frequency
Radio frequency has the lowest power requirements, can be transmitted relatively long distances (typically up to 10 km in rural locations) and does not cost for data usage
However, radio frequency requires another computer (a gateway) to receive the transmitted data, the gateway computer has a radio frequency receiver and is in a building with power and internet. The gateway computer uploads the received data to the database.
The Things Network https://www.thethingsnetwork.org/
  Creating a network of gateway computers around the world (LoRaWAN®)
  My understanding is then you just use a nearby LoRaWAN® gateway instead of requiring your own gateway computer
  Unsure how much this is used in industry

## Slide 17
5. Power supply

## Slide 18
Almost always Lithium-ion battery and solar panel, could be mains connected if not remote
Quantity of data seems to normally be limited by power constraints
  Biosphere water sensors changing data collection frequency summer / winter
5.a Battery and solar
2. Battery charger circuit, in: 5.5 V, out: 2.5–4.2 V
3. Batteries, 2.5-4.2 V
4. Microcontroller, with onboard voltage regulator
in: 2.5–4.2 V, regulated: 3.3 V
Solar, in: 5.5 V

## Slide 19
Conclusion
Sensor
Microcontroller
Physical property to measure
Temperature
Gas concentration
Distance
etc.
1
Send data
To local storage
Via mobile network
To central location
etc.
2
3
4
Connections and communication
2 power lines (positive & negative)
1-4 communication lines
Power supply
5